| Pistole pro velké zatížení Heavy Duty Safety Air Gun |  |
| --- | --- |
| Nové pistole Heavy Duty Safety Air Gun pro náročné použití jsou výkonné pistole pro dodání velké pracovní síly v prostředí těžkých provozů. Vstup tlakového vzduchu se závitem 3/8 NPT navyšuje proud vzduchu pomocí hubice (Super Air Nozzle), výsledkem je vyšší síla a proud vzduchu než u jiných pistolí. Odolné hliníkové tělo doplněné ergonomicky tvarovaným pryžovým držadlem a tvarovanou spouští umožňuje dlouhodobé použití bez únavy. Prodlužovací nástavec umožňuje širší možnosti použití. |  |

Model 1310-PEEK Heavy Duty Safety Air Gun (Model 1100-PEEK s Super Air Nozzle) Model 1310SS Heavy Duty Safety Air Gun (Model 1100SS s Super Air Nozzle) Model 1310 Heavy Duty Safety Air Gun (Model 1100 s Super Air Nozzle) Model 1210-PEEK používá Super Air Nozzle z plastu PEEK - chemicky odolné. Model 1210SS používá ocelové hubice (stainless steel Super Air Nozzle) pro náročné a korozivní prostředí. Spotřeba vzduchu Síla* Hladina hluku SCFM SLPM Ounces Gramy dBA 14 396 13 368 74 *Síla měřená ve vzdálenosti 12" (305mm) od cíle. Hladina hluku je měřena ve vzdálenosti 3' (914mm). Všechna měření provedena při 5.5 bar. Model 1330 Heavy Duty Safety Air Gun (s hubicí Model 1122 2" (51mm) Super Air Nozzle) Možnost: 1330SS s ocelovou (Stainless Steel 2" Super Air Nozzle) hubicí Spotřeba vzduchu Síla* Hladina hluku SCFM SLPM Unce Gramy dBA 22 622 22 624 77 *Síla měřená ve vzdálenosti 12" (305mm) od cíle. Hladina hluku je měřena ve vzdálenosti 3' (914mm). Všechna měření provedena při 5.5 bar. S 0.015" (0.38mm) vymezovací podložkou.Ploché provedení. Model 1350 Heavy Duty Safety Air Gun (s hubicí Model 1104 Super Air Nozzle) Možnost: 1350SS s ocelovou hubicí 3/8 NPT (Stainless Steel Super Air Nozzle) Spotřeba vzduchu Síla* Hladina hluku SCFM SLPM Unce Gramy dBA 35 991 30 850 82 *Síla měřená ve vzdálenosti 12" (305mm) od cíle. Hladina hluku je měřena ve vzdálenosti 3' (914mm). Všechna měření provedena při 5.5 bar. Model 1340 Heavy Duty Safety Air Gun (se složenou hlavicí Model 1111-4 Super Air Nozzle Cluster) Spotřeba vzduchu Síla* Hladina hluku SCFM SLPM Unce Gramy dBA 56 1585 3.2 1451 82 *Síla měřená ve vzdálenosti 12" (305mm) od cíle. Hladina hluku je měřena ve vzdálenosti 3' (914mm). Všechna měření provedena při 5.5 bar. Model 1360 Heavy Duty Safety Air Gun (s hubicí Model 1106 Super Air Nozzle) Možnost: 1360SS s 1/2 NPT ocelovou hubicí (Stainless SteelSuper Air Nozzle) Spotřeba vzduchu Síla* Hladina hluku SCFM SLPM Lbs. Gramy dBA 60 1699 3.3 1497 87 *Síla měřená ve vzdálenosti 12" (305mm) od cíle. Hladina hluku je měřena ve vzdálenosti 3' (914mm). Všechna měření provedena při 5.5 bar.

Přídavné nástavce (Add An Extension Pipe)

Pistole lze doplnit o nástavce pro prodloužení:

1. Vyberte model pistole (Heavy Duty Safety Air Gun). Příklad: Model 1310 2. Pro přidání nástavce, vytvořte nové modelové číslo přiřazením přídavného čísla (které znamená délku prodloužení) za číslo modelu pistole.

Příklad: Model 1310 Heavy Duty Safety Air Gun s 12" (305mm) hliníkovým nástavce (Aluminum Extension Pipe) je Model 1310-12.

Hliníkové nástavce Všechny pistole (Heavy Duty Safety Air Guns) s nástavci (Extension Pipes) se dodávají smontované Přídavné číslo -6 -12 -18 -24 -36 -48 -60 -72 Délka 6" (152mm) 12" (305mm) 18" (457mm) 24" (610mm) 36" (914mm) 48" (1219mm) 60" (1524mm) 72" (1829mm)

Pistole pro velká zatížení (Heavy Duty Safety Air Gun Models and Systems)

Heavy Duty Safety Air Gun s Model 1100 Model # Popis 1310 Heavy Duty Safety Air Gun with Model 1100 Super Air Nozzle 1310-6 Pistole Heavy Duty Safety Air Gun s hubicí Model 1100 Super Air Nozzle and 6" (152mm) Alum. nástav. 1310-12 Pistole Heavy Duty Safety Air Gun s hubicí Model 1100 Super Air Nozzle and 12" (305mm) Alum. nástav. 1310-18 Pistole Heavy Duty Safety Air Gun s hubicí Model 1100 Super Air Nozzle and 18" (457mm) Alum. nástav. 1310-24 Pistole Heavy Duty Safety Air Gun s hubicí Model 1100 Super Air Nozzle and 24" (610mm) Alum. nástav. 1310-36 Pistole Heavy Duty Safety Air Gun s hubicí Model 1100 Super Air Nozzle and 36" (914mm) Alum. nástav. 1310-48 Pistole Heavy Duty Safety Air Gun s hubicí Model 1100 Super Air Nozzle and 48" (1219mm) Alum. nástav. 1310-60 Pistole Heavy Duty Safety Air Gun s hubicí Model 1100 Super Air Nozzle and 60" (1524mm) Alum. nástav. 1310-72 Pistole Heavy Duty Safety Air Gun s hubicí Model 1100 Super Air Nozzle and 72" (1829mm) Alum. nástav.

Heavy Duty Safety Air Gun s Model 1100SS Model # Popis 1310SS Pistole Heavy Duty Safety Air Gun s hubicí Model 1100SS Super Air Nozzle 1310SS-6 Pistole Heavy Duty Safety Air Gun s hubicí Model 1100SS Super Air Nozzle and 6" (152mm) Alum. nástav. 1310SS-12 Pistole Heavy Duty Safety Air Gun s hubicí Model 1100SS Super Air Nozzle and 12" (305mm) Alum. nástav. 1310SS-18 Pistole Heavy Duty Safety Air Gun s hubicí Model 1100SS Super Air Nozzle and 18" (457mm) Alum. nástav. 1310SS-24 Pistole Heavy Duty Safety Air Gun s hubicí Model 1100SS Super Air Nozzle and 24" (610mm) Alum. nástav. 1310SS-36 Pistole Heavy Duty Safety Air Gun s hubicí Model 1100SS Super Air Nozzle and 36" (914mm) Alum. nástav. 1310SS-48 Pistole Heavy Duty Safety Air Gun s hubicí Model 1100SS Super Air Nozzle and 48" (1219mm) Alum. nástav. 1310SS-60 Pistole Heavy Duty Safety Air Gun s hubicí Model 1100SS Super Air Nozzle and 60" (1524mm) Alum. nástav. 1310SS-72 Pistole Heavy Duty Safety Air Gun s hubicí Model 1100SS Super Air Nozzle and 72" (1829mm) Alum. nástav.

Heavy Duty Safety Air Gun s Model 1100-PEEK Model # Popis 1310-PEEK Pistole Heavy Duty Safety Air Gun s hubicí Model 1100-PEEK Super Air Nozzle 1310-PEEK-6 Pistole Heavy Duty Safety Air Gun s hubicí Model 1100-PEEK Super Air Nozzle and 6" (152mm) Alum. nástav. 1310-PEEK-12 Pistole Heavy Duty Safety Air Gun s hubicí Model 1100-PEEK Super Air Nozzle and 12" (305mm) Alum. nástav. 1310-PEEK-18 Pistole Heavy Duty Safety Air Gun s hubicí Model 1100-PEEK Super Air Nozzle and 18" (457mm) Alum. nástav. 1310-PEEK-24 Pistole Heavy Duty Safety Air Gun s hubicí Model 1100-PEEK Super Air Nozzle and 24" (610mm) Alum. nástav. 1310-PEEK-36 Pistole Heavy Duty Safety Air Gun s hubicí Model 1100-PEEK Super Air Nozzle and 36" (914mm) Alum. nástav. 1310-PEEK-48 Pistole Heavy Duty Safety Air Gun s hubicí Model 1100-PEEK Super Air Nozzle and 48" (1219mm) Alum. nástav. 1310-PEEK-60 Pistole Heavy Duty Safety Air Gun s hubicí Model 1100-PEEK Super Air Nozzle and 60" (1524mm) Alum. nástav. 1310-PEEK-72 Pistole Heavy Duty Safety Air Gun s hubicí Model 1100-PEEK Super Air Nozzle and 72" (1829mm) Alum. nástav.

Heavy Duty Safety Air Gun s Model 1122 Model # Popis 1330 Pistole Heavy Duty Safety Air Gun s hubicí Model 1122 2" (51mm) Super Air Nozzle 1330-6 Pistole Heavy Duty Safety Air Gun s hubicí Model 1122 2" (51mm) Super Air Nozzle and 6" (152mm) Al. nástav. 1330-12 Pistole Heavy Duty Safety Air Gun s hubicí Model 1122 2" (51mm) Super Air Nozzle and 12" (305mm) Al. nástav. 1330-18 Pistole Heavy Duty Safety Air Gun s hubicí Model 1122 2" (51mm) Super Air Nozzle and 18" (457mm) Al. nástav. 1330-24 Pistole Heavy Duty Safety Air Gun s hubicí Model 1122 2" (51mm) Super Air Nozzle and 24" (610mm) Al. nástav. 1330-36 Pistole Heavy Duty Safety Air Gun s hubicí Model 1122 2" (51mm) Super Air Nozzle and 36" (914mm) Al. nástav. 1330-48 Pistole Heavy Duty Safety Air Gun s hubicí Model 1122 2" (51mm) Super Air Nozzle and 48" (1219mm) Al. nástav. 1330-60 Pistole Heavy Duty Safety Air Gun s hubicí Model 1122 2" (51mm) Super Air Nozzle and 60" (1524mm) Al. nástav. 1330-72 Pistole Heavy Duty Safety Air Gun s hubicí Model 1122 2" (51mm) Super Air Nozzle and 72" (1829mm) Al. nástav.

Heavy Duty Safety Air Gun s Model 1122SS Model # Popis 1330SS Pistole Heavy Duty Safety Air Gun s hubicí Model 1122SS 2" (51mm) Super Air Nozzle 1330SS-6 Pistole Heavy Duty Safety Air Gun s hubicí Model 1122SS 2" (51mm) Super Air Nozzle and 6" (152mm) Al. nástav. 1330SS-12 Pistole Heavy Duty Safety Air Gun s hubicí Model 1122SS 2" (51mm) Super Air Nozzle and 12" (305mm) Al. nástav. 1330SS-18 Pistole Heavy Duty Safety Air Gun s hubicí Model 1122SS 2" (51mm) Super Air Nozzle and 18" (457mm) Al. nástav. 1330SS-24 Pistole Heavy Duty Safety Air Gun s hubicí Model 1122SS 2" (51mm) Super Air Nozzle and 24" (610mm) Al. nástav. 1330SS-36 Pistole Heavy Duty Safety Air Gun s hubicí Model 1122SS 2" (51mm) Super Air Nozzle and 36" (914mm) Al. nástav. 1330SS-48 Pistole Heavy Duty Safety Air Gun s hubicí Model 1122SS 2" (51mm) Super Air Nozzle and 48" (1219mm) Al. nástav. 1330SS-60 Pistole Heavy Duty Safety Air Gun s hubicí Model 1122SS 2" (51mm) Super Air Nozzle and 60" (1524mm) Al. nástav. 1330SS-72 Pistole Heavy Duty Safety Air Gun s hubicí Model 1122SS 2" (51mm) Super Air Nozzle and 72" (1829mm) Al. nástav.

Heavy Duty Safety Air Gun s Model 1111-4 Model # Popis 1340 Pistole Heavy Duty Safety Air Gun s hubicí Model 1111-4 Super Air Nozzle Cluster 1340-6 Pistole Heavy Duty Safety Air Gun s hubicí Model 1111-4 Super Air Nozzle Cluster and 6" (152mm) Alum. nástav. 1340-12 Pistole Heavy Duty Safety Air Gun s hubicí Model 1111-4 Super Air Nozzle Cluster and 12" (305mm) Alum. nástav. 1340-18 Pistole Heavy Duty Safety Air Gun s hubicí Model 1111-4 Super Air Nozzle Cluster and 18" (457mm) Alum. nástav. 1340-24 Pistole Heavy Duty Safety Air Gun s hubicí Model 1111-4 Super Air Nozzle Cluster and 24" (610mm) Alum. nástav. 1340-36 Pistole Heavy Duty Safety Air Gun s hubicí Model 1111-4 Super Air Nozzle Cluster and 36" (914mm) Alum. nástav. 1340-48 Pistole Heavy Duty Safety Air Gun s hubicí Model 1111-4 Super Air Nozzle Cluster and 48" (1219mm) Alum. nástav. 1340-60 Pistole Heavy Duty Safety Air Gun s hubicí Model 1111-4 Super Air Nozzle Cluster and 60" (1524mm) Alum. nástav. 1340-72 Pistole Heavy Duty Safety Air Gun s hubicí Model 1111-4 Super Air Nozzle Cluster and 72" (1829mm) Alum. nástav.

Heavy Duty Safety Air Gun s Model 1104 Model # Popis 1350 Pistole Heavy Duty Safety Air Gun s hubicí Model 1104 Super Air Nozzle 1350-6 Pistole Heavy Duty Safety Air Gun s hubicí Model 1104 Super Air Nozzle and 6" (152mm) Alum. nástav. 1350-12 Pistole Heavy Duty Safety Air Gun s hubicí Model 1104 Super Air Nozzle and 12" (305mm) Alum. nástav. 1350-18 Pistole Heavy Duty Safety Air Gun s hubicí Model 1104 Super Air Nozzle and 18" (457mm) Alum. nástav. 1350-24 Pistole Heavy Duty Safety Air Gun s hubicí Model 1104 Super Air Nozzle and 24" (610mm) Alum. nástav. 1350-36 Pistole Heavy Duty Safety Air Gun s hubicí Model 1104 Super Air Nozzle and 36" (914mm) Alum. nástav. 1350-48 Pistole Heavy Duty Safety Air Gun s hubicí Model 1104 Super Air Nozzle and 48" (1219mm) Alum. nástav. 1350-60 Pistole Heavy Duty Safety Air Gun s hubicí Model 1104 Super Air Nozzle and 60" (1524mm) Alum. nástav. 1350-72 Pistole Heavy Duty Safety Air Gun s hubicí Model 1104 Super Air Nozzle and 72" (1829mm) Alum. nástav.

Heavy Duty Safety Air Gun s Model 1104SS Model # Popis 1350SS Pistole Heavy Duty Safety Air Gun s hubicí Model 1104SS Super Air Nozzle 1350SS-6 Pistole Heavy Duty Safety Air Gun s hubicí Model 1104SS Super Air Nozzle and 6" (152mm) Alum. nástav. 1350SS-12 Pistole Heavy Duty Safety Air Gun s hubicí Model 1104SS Super Air Nozzle and 12" (305mm) Alum. nástav. 1350SS-18 Pistole Heavy Duty Safety Air Gun s hubicí Model 1104SS Super Air Nozzle and 18" (457mm) Alum. nástav. 1350SS-24 Pistole Heavy Duty Safety Air Gun s hubicí Model 1104SS Super Air Nozzle and 24" (610mm) Alum. nástav. 1350SS-36 Pistole Heavy Duty Safety Air Gun s hubicí Model 1104SS Super Air Nozzle and 36" (914mm) Alum. nástav. 1350SS-48 Pistole Heavy Duty Safety Air Gun s hubicí Model 1104SS Super Air Nozzle and 48" (1219mm) Alum. nástav. 1350SS-60 Pistole Heavy Duty Safety Air Gun s hubicí Model 1104SS Super Air Nozzle and 60" (1524mm) Alum. nástav. 1350SS-72 Pistole Heavy Duty Safety Air Gun s hubicí Model 1104SS Super Air Nozzle and 72" (1829mm) Alum. nástav.

Heavy Duty Safety Air Gun s Model 1106 Model # Popis 1360 Pistole Heavy Duty Safety Air Gun s hubicí Model 1106 Super Air Nozzle 1360-6 Pistole Heavy Duty Safety Air Gun s hubicí Model 1106 Super Air Nozzle and 6" (152mm) Alum. nástav. 1360-12 Pistole Heavy Duty Safety Air Gun s hubicí Model 1106 Super Air Nozzle and 12" (305mm) Alum. nástav. 1360-18 Pistole Heavy Duty Safety Air Gun s hubicí Model 1106 Super Air Nozzle and 18" (457mm) Alum. nástav. 1360-24 Pistole Heavy Duty Safety Air Gun s hubicí Model 1106 Super Air Nozzle and 24" (610mm) Alum. nástav. 1360-36 Pistole Heavy Duty Safety Air Gun s hubicí Model 1106 Super Air Nozzle and 36" (914mm) Alum. nástav. 1360-48 Pistole Heavy Duty Safety Air Gun s hubicí Model 1106 Super Air Nozzle and 48" (1219mm) Alum. nástav. 1360-60 Pistole Heavy Duty Safety Air Gun s hubicí Model 1106 Super Air Nozzle and 60" (1524mm) Alum. nástav. 1360-72 Pistole Heavy Duty Safety Air Gun s hubicí Model 1106 Super Air Nozzle and 72" (1829mm) Alum. nástav.

Heavy Duty Safety Air Gun s Model 1106SS Model # Popis 1360SS Pistole Heavy Duty Safety Air Gun s hubicí Model 1106SS Super Air Nozzle 1360SS-6 Pistole Heavy Duty Safety Air Gun s hubicí Model 1106SS Super Air Nozzle and 6" (152mm) Alum. nástav. 1360SS-12 Pistole Heavy Duty Safety Air Gun s hubicí Model 1106SS Super Air Nozzle and 12" (305mm) Alum. nástav. 1360SS-18 Pistole Heavy Duty Safety Air Gun s hubicí Model 1106SS Super Air Nozzle and 18" (457mm) Alum. nástav. 1360SS-24 Pistole Heavy Duty Safety Air Gun s hubicí Model 1106SS Super Air Nozzle and 24" (610mm) Alum. nástav. 1360SS-36 Pistole Heavy Duty Safety Air Gun s hubicí Model 1106SS Super Air Nozzle and 36" (914mm) Alum. nástav. 1360SS-48 Pistole Heavy Duty Safety Air Gun s hubicí Model 1106SS Super Air Nozzle and 48" (1219mm) Alum. nástav. 1360SS-60 Pistole Heavy Duty Safety Air Gun s hubicí Model 1106SS Super Air Nozzle and 60" (1524mm) Alum. nástav. 1360SS-72 Pistole Heavy Duty Safety Air Gun s hubicí Model 1106SS Super Air Nozzle and 72" (1829mm) Alum. nástav.